## Slide 1
Logic Synthesis Using
Cadence Genus Tool

## Slide 2
RTL code
(.v file)
Attributes & Constraints
(timing)
GENUS
Synthesis Tool
Optimized Design :
Mapped verilog
(Gate-level Netlist)
Reports (Timing Area, Power…etc.)
Timing Library
(.Lib file)
Synopsys design constraint file
(.sdc format)

## Slide 3
Genus Optimization Goals
Timing
  Top -most optimization criteria  Timing
Ungrouping
  set_attribute auto_ungroup none /
  set_attribute ungroup_ok false <instance/subdesign>
Boundary Optimization
  boundary_opto (subdesign) boundary_optimize_constant_hier_pins(subdesign/pin) boundary_optimize_equal_opposite_hier_pins(subdesgin/pin)
  boundary_optimize_feedthrough_hier_pins (subdesgin/pin) boundary_optimize_invert_hier_pins (subdesgin/pin)

## Slide 4
Datapath Optimization
  set_attribute user_speed_grade very_fast <datapath_module>
Path Grouping
  define_cost_group -name in2reg
  path_group -from [all_inputs] -group in2reg
  define_cost_group -name reg2out
  path_group -to [all_outputs] -group reg2out
TNS Optimization
  set_attribute tns_opto true

## Slide 5
Incremental Optimization
  Multiple incremental synthesis runs help to improve timing result.
Retiming
  Registers are repositioned to reduce cycle time or area.
  Used for pipelined designs.
Path Adjust
  To optimize a selective path
  path_adjust -delay <delay> -from <start_point> -to <end_point>
Cell Biasing
  To use complex cells ( set the value to <1)
  set_attribute area_multiplier

## Slide 6
Power
  Power optimization is not enabled by default.
  Optimizes power constraints for leakage power and dynamic power set by the attributes
  max_leakage_power & max_dynamic_power.
Area
  smallest design that satisfies the timing constraint by default
  set_max_area
  logic in the non-critical paths is automatically downsized to save area